## Slide 1: Multicore Reference Architecture – Breakout Session Summary

## Slide 2: Motivation
Summarize the currently used multicore strategies within Div E, Div A, Div C and Div U
Find common aspect and the differences
Collect potential topics for reference architecture

## Slide 3: Division E – Multicore
Core 0
Core 1
Core 2
Core 3
ASS - Mixed Asil (Split 1)
HWnSW – AsilC
Inverter & EMF Safety
ASS
ASS - Mixed Asil (Split 2)
Edrive - AsilC
Edrive – QM
ASS
EMF
OEM
Edrive – AsilB
ASS
Inverter
EMF
Edrive – Qm
Inverter
Edf
Emf
BSW, MCAL Stack
RTE (IoC)
Multicore is used primarily used to solve CPU load balancing problem
Core distribution is not done primarily to partition different ASIL compositions
For inter-core communication RTE/IOC mechanism is used
Scope of optimization using std IPC

## Slide 4: Division U
Core 0
Core 1/DSP
Core 2/DSP
…
BSW, MCAL Stack
Signal Processing
Perception
RTE
veIPC
Core distribution is primarily done for splitting the DSP based algorithms for performance (mostly async)
No AUTOSAR on performance cores
Safety is managed with Master core and Vector stack provided mechanisms
veIPS and Interrupt-Sync shared memory is used for inter core communications
Product-specific HW/SW solutions (TI offers an ICC HW infrastructure on its Micro and corresponding SW drivers for the cores)
SWC

## Slide 5: Summary of Common Aspects
Core distribution done for load balancing as well as to address safety requirement
Microcontroller Hardware Environment: Infineon Aurix (Div A, Div E, Div U, Div C)
Middleware Environment: Vector MICROSAR solution with multicore support
Customer application software in most cases provided by OEMs to integrate on project
Safety partitoning done on lock step core and sometimes even on non-step core (upto ASIL B)

## Slide 6: Topics for Reference Architecture
  Hardware prereferral access from multiple cores; address concurrent and exclusive needs
  Standardized and scalable IPC mechanism [Combination of vIPC + RTE/Spinlocks + ZF Optimized RTE]
  Common, configurable architecture of EH, BSAB, CDD and MWL components
  Standardization for Safety deployment with dedicated core; independent OsApplication approach
  Standardization of L3 micro-controller monitoring mechanism; controller or family specific implementation

## Slide 7: ZF Basic SW Components
Components | Multicore Readiness | Concept
EH | Yes | Master-Satellite
CDD | Yes | Master-Satellite
MWL | Yes | OsApps
BSAB | To be checked | 

## Slide 8: Error H andler – Multicore Readiness
EH has rich feature set and hence used widely - ASIL C capable, OBD capable ERRH (Highly configurable for APPL engineers)
2nd implementation developed by PLZ with more satellite concepts
One satellite per OS Applications is possible.
Master and 5 satellites are currently also used
Master and 2 satellites supplied to PE - OsAppl was introduced and thus satellites were added
Constraints: DCM/Tester communication should be done from same core from where the Master is located
Latest release is being used by Audi PPE and BMW Gen6 with multicore support
Pre-processor and switches are used for manual configurations, std files are not used for configurations of EH