## Slide 1: SoA Reference Architecture Layers

## Slide 2: Service Oriented Architecture V1.1
Operating System
Middleware Stack
Hardware (HPC)
Platform Software (Drivers, Platform libraries, Hypervisor)
Bootloader
Application Components
Application Layer
Middleware Layer
Customer
and 3rd party
ZF Functions, Software products or engineering
MW Stack
Application Service Components
System Service Components
Platform specific applications and libraries:, like drivers, frame server, fan control.
Hardware Support Layer
All Programs running inside Function adapter
Middleware Stack includes Service Manager, it queries platform layer for capabilities, it is stable, executable and dynamically configurable
Adaption to different HW and device abstraction.
Application component examples are trajectory planning, lane centering.
Application service component examples are perception, cubiX, System functions (e.g. BMW System Function Modules)
System Service Components examples are CAN-dbc implementations, Diagnostic Management, Mode Management, …
(Feature)
(Function)
Type 1 Hypervisor to run Guest OS like POSIX, Linux and Android
SoC

## Slide 3: Proposal - Functional Architecture ADAS/AD
USS
CAM
Lidar
Radar
Vehicle Network
HCP – IDC8 incl SoC (SµC & SoC)
Middleware, AutoSAR (classic/adaptive), Custom (MB.os)
Operating System OS (QNX, certif. Linux, SAFERTOS..)
Sensor Abstraction and Low Level Processing
Fusion
Perception
Localization
AD Map
Environment Model
HMI
Vehicle Motion Mgmt
Vehicle Management
Vehicle Actuator Control
L2(+) Driving Function
NCAP (AEB, ACC, Traffic Jam pilot…)
L3 Driving Function
Highway
Parking
L2 Parking Assits
L4 Valet Parking
L4/5 AD Driving
L4 Urban Driving
L4 InterUrban - Highway Pilot
Cloud / Services
Fleet Management
AD Map
Remote Control
ext. Perception
ShadowMode
Data Collection
Backend Host
Driving / Customer Functions Layer
ADAS / AD Base Function Layer
ADAS / AD Software Base Layer
Hardware / Vehicle Layer
Application Components
Application Service Components
System Service Components
Middleware Stack
Sensor and Actuator
Hardware Layer and SoC
Platform Layer

## Slide 4: Service Oriented Architecture V1.0
Operating System
Middleware Stack
HPC incl SoC (SµC & SoC)
Platform Software ( Drivers, Platform libraries, Hypervisor )
Application Components
Application Layer
Customer
and 3rd party
ZF Functions, Software products or engineering
Application Service Components
System Service Components
All Programs running inside Function adapter
Application component examples are trajectory planning, lane centering.
Application service component examples are perception, cubiX, System functions (e.g. BMW System Function Modules)
Middleware Layer
Middleware Stack includes Service Manager, it queries platform layer for capabilities, it is stable, executable and dynamically configurable
System Service Components examples are CAN-dbc implementations, Diagnostic Management, Mode Management, …
(Feature)
(Function)
Platform specific applications and libraries:, like drivers, frame server, fan control.
Hardware Support Layer
Adaption to different HW and device abstraction.
Type 1 Hypervisor to run Guest OS like POSIX, Linux and Android
L3 Driving Function
Highway
Parking
L2 Parking Assits
L4 Valet Parking
L4/5 AD Driving
L4 Urban Driving
L4 InterUrban - Highway Pilot
L2(+) Driving Function
NCAP (AEB, ACC, Traffic Jam pilot…)
Sensor Abstraction
Middleware, AutoSAR (classic/adaptive), Custom (MB.os)
Operating System OS (QNX, certif. Linux, SAFERTOS..)
Fusion
Perception
Localization
AD Map
Environment Model
HMI
Vehicle Motion Mgmt
Vehicle Management
Vehicle Actuator Control

## Slide 5: Questionnaire Summary for Reference Architecture
Interview for actual architecture and update of Questionnaire is planned for the following Divisions:
  Division U (Mr. Kraemer Ulrich & Mr. ACHIR Mounir) on 28th April 2022 --> Done
  Division XA (Mr. Dohrmann Stephan) on 2nd May 2022 --> Done
  Division XA (Mr. Oprisan Dan) --> In Progress ( Planned meeting on 6th May 2022 )
  Division U Perception Team (Mr. Nico Stock) --> In Progress ( Planned to schedule based on availability )
  Division U Perception Team (Mr. Carsten Hass) --> In Progress ( Planned to schedule based on availability )

## Slide 6: SOA Discussion Result with U Division
Attendees :-
Kraemer Ulrich KBL UDAS392 ulrich.kraemer@zf.com (U Division)
ACHIR Mounir KBL UDAS3 Mounir.Achir@zf.com (U Division)
Geiger Roland Dr. FRD DISS1 roland.geiger@zf.com
Joshi Pratikkumar pratikkumar.joshi.external@zf.com
Bujone Akshay akshay.bujone.external@zf.com
Gole Sachin sachin.gole.external@zf.com
RFQ is more towards cost driven where it is requested to reduce the size of Micro to save the cost
Direction is to have reduced memory for the ECUs (remove not requested SW functions)
Current projects are Classic AutoSAR, camera and sensor based where SOA will not be applicable
For long term, SOA can be considered with hardware resource capabilities needed
Dusseldorf team works on Driving functions and Central ECU platform where SOA can be utilized
In U Division currently they have Classic AutoSAR project, in short term they don’t have project where SOA is needed, current direction to have further reduction of ECU cost and memory.

## Slide 7: SOA Discussion Result with XA Division
Attendees :-
Dohrmann Stephan FRD XAXE2 stephan.dohrmann@zf.com (XA Division)
Geiger Roland Dr. FRD DISS1 roland.geiger@zf.com
Joshi Pratikkumar pratikkumar.joshi.external@zf.com
Bujone Akshay akshay.bujone.external@zf.com
Gole Sachin sachin.gole.external@zf.com
Vector AUTOSAR Adaptive platform is used in current projects.
Feature/functions are using ara::com middleware for communication defined by Vector Adaptive stack
Vector Adaptive stack limitation and drawback already taken care by implementing modules like shared memory, zero copy, Faster communication using UDP socket in SOME/IP.
XA team has suggested come up with code examples where they would like to see how Application Service component and System service component can be implemented and how they communicate with each other.

## Slide 8: Service Oriented Architecture Middleware
Asynchronous Remote Procedure Call
SOA Consumer
Middleware
Middleware
SOA Provider
Ethernet
HPC / ECU
HPC / ECU

## Slide 9: Service Oriented Architecture
Service Broker
Service Provider
Service Consumer
Publish
Find
Bind
Internet / Ethernet
Service Provider
Service Consumer
Service Registry
Offer
Find
Call (RPC)
Communication Pattern and Service Discovery

## Slide 10: Service Oriented Architecture
Deployment View
Feature 1
Feature 2
Functions (Shared object / Lib)
Service Oriented Architecture Middleware
SOME/IP Communication Middleware
Inter Process Communication Middleware
DDS Communication Middleware
Protocol Binding
SOA App Process
Feature 3
SOA App Process
SOA App Process
Guest OS
Guest OS
Type 1 Hypervisor
Classic AutoSAR OS
RTOS
SOA App Process
Feature X
Cortex-A CPU
Cortext-M CPU